## Slide 1
MICROPROCESSOR-8085 AND ITS WORKING
By Partha Pratim Dey

## Slide 2: Content
Introduction
Features
Pin Configuration
Architecture 0f 8085
The 8085 Bus Structure
8085 Interrupts
Use of Microprocessor

## Slide 3: Introduction
Microprocessor is a Central Processing Unit (CPU) etched on a single chip. A single Integrated Circuit (IC) has all the functional components of a CPU namely Arithmetic Logic Unit (ALU), Control Unit and registers. The 8085 microprocessor is an 8-bit processor that includes on its chip most of the logic circuitry for performing computing tasks and for communicating with peripherals.

## Slide 4: Features
8 bit microprocessor(8085 microprocessor can read or write or perform arithmetic and logical operations on 8-bit data at time)
It has 8 data lines and 16 address lines hence capacity is 216 = 64 kB of memory
Cock frequency is 3 MHz
It requires +5V power supply.
It provides 5 hardware interrupt and 8 so ftware interrupts.

## Slide 5: Pin Configuration
40 pins classified into
6 groups:
Data bus
Address bus
Control & status lines
Externally generated
Serial interface
Power supply & clock

## Slide 6: Pin Configuration cont…
1) Address Bus (A15-A8 and AD7-AD0):
The microprocessor 8085 has 16 bit address lines from A15-A8 and AD7-AD0. These lines are used to transfer 16 bit address of memory as well as 8-bit address of I/O ports.
2) Data Bus:
The lower 8 lines (AD7-AD0) are often called as multiplexed data lines.

## Slide 7
CONTROL LINES
RD : Read: This is active low signal which indicates that the selected I/O or memory device is to be read and also is available on the data bus.
WR : Write: This is active low signal which indicates that the data on data bus are to be written into a selected memory location.
IO/ M : (Input / Output / Memory): This is used to select either Input / Output devices or memory operation. When it is high it indicates an I/O operation and when it is low, it indicates a memory operation.
STATUS LINES
Status Pins (S1, S0): The microprocessor 8085 has two status pins as S1, S0 which is used to indicate the status of microprocessor or operation which is performed by microprocessor.

## Slide 8
SPECIAL SIGNAL
ALE (Address Latch Enable): The ALE signal is used to enable or disable the external latch IC (74373/8212).
The external latch IC is used for the de-multiplexing of AD7-AD0 lines, i.e., it is used to separate the address and data from AD7-AD0 lines.
If ALE = 1/0 then external latch IC is enabled / disabled respectively.

## Slide 11: Architecture 0f 8085
ALU
Timing and Control Unit
General Purpose Registers
Program Status word
Program Counter
Stack Pointer
Instruction Register and Decoder
8. Interrupt Control
9.Serial I/O Control
10.Address Bus
11. Data Bus

## Slide 12: REGISTERS
The Registers are of 8-bit & 16-bit size used for different purposes
  A- Accumulator – This is an special purpose register. All the ALU operations are performed with reference to the contents of Accumulator.
  B,C,D,E,H,L – General purpose registers. These registers can also used for 16-bit operations in pairs. The default pairs are BC, DE & HL.

## Slide 13
  F – Flag register – This register indicates the status of the ALU operation.
  PC – Program Counter – This is a 16-bit register used to address the memory location from where an instruction is going to be executed.

## Slide 14
  SP – Stack pointer - This is a 16-bit register used to address the top of the stack memory location.
  Temporary register, W & Z – These registers are only used by 8085 and are not available for the programmer.

## Slide 15
ALU – Arithmetic & Logic Unit
  ALU of 8085 performs 8-bit arithmetic & logical operations. The operations are generally performed with Accumulator as one of the operands. The result is saved in accumulator register.
Timing & Control Unit
  This unit works as the brain of the CPU and generates all the timing and control signals to perform all the internal & external operations of the CPU.
Instruction Decoder & Machine Cycle Encoder Unit
  This unit decodes the op-code stored in the Instruction Register (IR) and encodes it for the timing & control unit to perform the execution of the instruction.

## Slide 16: The 8085 Bus Structure
The 8-bit 8085 CPU (or MPU – Micro Processing Unit) communicates with the other units using a 16-bit address bus, an 8-bit data bus and a control bus.

## Slide 17: 8085 Interrupts
Vector interrupt − In this type of interrupt, the interrupt address is known to the processor. For example: RST7.5, RST6.5, RST5.5, TRAP.
Non-Vector interrupt − In this type of interrupt, the interrupt address is not known to the processor so, the interrupt address needs to be sent externally by the device to perform interrupts. For example: INTR.
Maskable interrupt − In this type of interrupt, we can disable the interrupt by writing some instructions into the program. For example: RST7.5, RST6.5, RST5.5.
Non-Maskable interrupt − In this type of interrupt, we cannot disable the interrupt by writing some instructions into the program. For example: TRAP.
Software interrupt − In this type of interrupt, the programmer has to add the instructions into the program to execute the interrupt. There are 8 software interrupts in 8085, i.e. RST0, RST1, RST2, RST3, RST4, RST5, RST6, and RST7.
Hardware interrupt − There are 5 interrupt pins in 8085 used as hardware interrupts, i.e. TRAP, RST7.5, RST6.5, RST5.5, INTA.

## Slide 18: Use of Microprocessor
Calculators
Games machine
Complex Industrial Controllers
Traffic light Control
Multi user, multi-function environments
Military applications
Communication systems